## Slide 1: Vibration Analysis

## Slide 2
Purpose of Vibration Analysis
To Identify Health Condition
To detect the defects and
Inaccuracies
To Pinpoint the Defective
locations

## Slide 3
PROBLEMS ON MY MACHINES
NO

## Slide 4
VIBRATION
ONLY PROBLEM IS

## Slide 5
“VIBRATION ANALYSIS”
ALONE CAN IDENTIFY
> 95%
OF MACHINERY PROBLEMS

## Slide 6
Basic Theory Of Vibration
Simple Spring Mass System
Upper
Limit
Neutral
Position
Lower
Position
Displacement
Max Acc
Mim Vel
Max Acc
Mim Vel
Max Vel
Mim Acc
It follows sine curve.

## Slide 7: Time Waveform
1 revolution
Time
Amplitude
0
+
-
3600 RPM = 3600 cycles per minute
60 Hz = 60 cycles per second
1 Order = One times turning speed
Heavy Spot
Rotation

## Slide 8: Frequency & Amplitude
Frequency:
How many times oscillation is occurring
for a given time period?
Units: Cycles Per Sec or Hertz, CPM
Amplitude:
It is the magnitude of vibration signal.
Units: Micron, MM/Sec, g’s or M/Sec2

## Slide 9: Physical Significance Of Vibration Characteristics
Frequency - What is vibrating?
Source of the vibration.
Amplitude - How much is it vibrating?
Size (severity) of the problem.
Phase Angle - How is it vibrating?
Cause of the vibration.

## Slide 10
60 RPM
= 1 Rev / s
= 1 Hz
Frequency Measurement

## Slide 11: Amplitude Measurement
1. Displacement :
The distance a structure moves or vibrates from its reference or rest position.
Unit : Microns(p-p), mils(p-p)
2. Velocity :
Rate of change of displacement. It is the
measure of the speed at which the mass is
vibrating during its oscillation.
Unit : MM/Sec, Inch/sec (RMS or Peak)
3. Acceleration :
It is the rate of change of velocity. The
greater the rate of change of velocity the
greater the forces (F=ma) on the machines.
Unit : M/Sec2, Inch/sec2 , g’s (RMS)

## Slide 12
B
C
A
a
b
c
t
t
t

## Slide 13
t
+
a
d
v

## Slide 14: Physical Significance Of Vibration Amplitude
Displacement : Stress Indicator
Velocity : Fatigue Indicator
Acceleration : Force Indicator

## Slide 16
VIBRATION SENSITIVITY
DISPLACEMENT
VELOCITY
ACCELERATION
FREQUENCY
CPM
60 600 6000 60000 600 000
10
1
.1
.01
.001
When To Use Disp., Vel. & Acc.?

## Slide 17: What Is The Advantage Of Using Velocity?
Flat frequency range compared to displacement & acceleration.
Almost all machines generate fault frequency between 600CPM to 60KCPM
Velocity indicates fatigue.
Velocity is the best indicator of vibration severity.

## Slide 18: Scales Of Amplitude
Peak
Peak to Peak
RMS
Av.
Peak - a
Peak to Peak - 2a
RMS - 0.707 a
Average - 0.637 a

## Slide 19: Vibration Transducers
Produces electrical signal of vibratory motion
Proximity Probe - Displacement
Velocity Probe - Velocity
Accelerometer - Acceleration

## Slide 20: Proximity Probe

## Slide 21
Permanently installed on large machines with sleeve bearings.
Measures relative displacement between the bearing housing(probe tip) and the rotating shaft.
Called Eddy Current Probe
Frequency range 0 to 60,000 CPM

## Slide 22
Velocity Probe

## Slide 23
Oldest of all.
Produces signal proportional to velocity.
Self generating and needs no conditioning electronics.
It is heavy, complex and expensive.
Frequency response from 600CPM to 60,000CPM
Temperature sensitive

## Slide 24: Accelerometer

## Slide 25
Produces signal proportional to acceleration of seismic mass.
Extremely linear amplitude sense.
Large Frequency range
Smaller in size

## Slide 26: Time Waveform
1 revolution
Time
Amplitude
0
+
-
3600 RPM = 3600 cycles per minute
60 Hz = 60 cycles per second
1 Order = One times turning speed
Heavy Spot
Rotation

## Slide 27: Time Waveform
1000 RPM
1 revolution
Time
Amplitude
0
+
-
4 blades = Vibration occurs 4 times per revolution
4 X 1000 RPM = Vibration occurs at 4000 cycles per minute
= 4000 CPM

## Slide 28: Time Waveform
12 tooth gear
1000 RPM
1 revolution
Time
Amplitude
0
+
-
12 teeth are meshing every revolution of the gear
12 x 1000 RPM = vibration occurs at 12,000 cycles per minute
= 12,000 cpm = 200 Hz

## Slide 29: Time Waveform
Time
0
+
-
Time
Time
0
+
-
0
+
-

## Slide 30: Time Waveform
0
-
+
Time
Time Waveform contains all the different frequencies mixed together.

## Slide 31: Time Waveform
Example of a time waveform

## Slide 32: Signal Acquisition
Transducer
Overall
Energy
FFT
Waveform
Spectrum
Amplitude
Amplitude
Time
Frequency

## Slide 33: FFT SPECTRUM A calculation method of converting a time waveform to a frequency display that shows the relationship of discrete frequencies and their amplitudes

## Slide 34: Frequency Domain
FFT - Fast Fourier Transform
Separates individual frequencies
Detects how much vibration at each frequency

## Slide 35: FFT Signal Processing

## Slide 36: Frequency Domain
Frequency
1x
4x
12x
Time
0
+
-
Time
Time
0
+
-
0
+
-
Frequency
Frequency

## Slide 37: A Typical FFT Spectrum
Many distinct peaks

## Slide 38: A Typical FFT Spectrum
Specific peaks typically correlate to
Specific machine faults
Related to machine speed

## Slide 39: Phase

## Slide 40: What Is Phase?
Phase is a measure of relative time difference between two sine waves.
Trigger Any event which can be used as a timing reference.
Keyphasor ( phase reference sensor ) A signal used in rotating machinery measurements , generated by a sensor observing a once per revolution event .

## Slide 41: Importance Of Phase
Phase is a relative measurement.
Provides information how one part of a machine is vibrating compared to other.
Confirmatory tool for problems like-
1. Unbalance
2. Misalignment
3. Eccentric Rotor, Bent Shaft.
4. Mechanical Looseness, Structural Weakness, Soft Foot.
5. Resonance.
6. Cocked bearing.
No correlation with Bearing defects, Gear defects,
Electrical motor defect.

## Slide 42: How Phase Angle Is Measured?
The Phase Angle is the angle (in degrees) the
shaft travels from the start of data collection to
when the sensor experiences maximum positive
force.
For example, the phase angle is 90° if the sensor
experiences its maximum positive force at 90°
after data collection was initiated by the
tachometer.

## Slide 43
We are Machine Doctors

## Slide 44: Diagnosing Machine Faults
Unbalance
Misalignment
General looseness or wear
Bearing defects
Gear defects
Belt defects
Electrical Faults
Journal Bearing Faults
Resonance

## Slide 45: Unbalance

## Slide 46: What is unbalance?
Rotation
Heavy Spot
Center of Mass = Center of Rotation
Center of Mass
Center of Shaft
The force created by a rotating body when its center of mass is offset from its center of rotation

## Slide 47: Causes of unbalance
Improper assembly
Material Buildup
Wear
Broken or missing parts

## Slide 48: Characteristics of unbalance
  High radial peaks at 1X shaft RPM
  Low axial vibration at 1X shaft RPM
  Low harmonics of shaft RPM
  1X RPM sinusoidal pattern in the time waveform
  Can cause other faults to appear, especially looseness

## Slide 49: Unbalance
Imbalance
Imbalance typically appears at
the turning speed of the machine

## Slide 50: Unbalance
Freq: 60.04 Hz
Order: 1.010
Spec: .390
Radial vibration at 1X shaft RPM is much more significant than in the axial direction

## Slide 51: What is Misalignment?
Deviation from a common centerline during operation.

## Slide 53: Types of Misalignment
Angular
Both
Offset

## Slide 54: Misalignment
Characteristics:
  High axial levels
  High axial at 1, 2 and 3X shaft RPM
  High radial at 1, 2 and 3X shaft RPM
  Repeatable periodic waveform with one or two clear peaks per revolution
  Phase readings show a 180o shift across the coupling

## Slide 55
Angular - Axial vibration at 1X RPM
Offset - Radial vibration at 2X or 3X RPM
Harmonics (3X-10X) generates as severity increases.
If the 2X amplitude more than 50% of 1X then
coupling damage starts.
If the 2X amplitude more than 150% of 1X then
machine should be stopped for correction.
Misalignment: Characteristics

## Slide 56: Misalignment
Misalignment
Misalignment typically shows up
at either 1 or 2 x turning speeds

## Slide 57: Misalignment
Freq: 59.50
Order: 2.010
Spec: .640
Vane Pass
2X shaft RPM is dominant location of vibration
Vane pass is due to 11 blade pump impeller

## Slide 58: Mechanical Looseness

## Slide 59: Causes
It alone can not create vibration but in the influence of Unbalance, Misalignment, Bearing problems it amplify the amplitude.
It should be corrected first.

## Slide 60: Types of Looseness
Structural Looseness
- Base mount
- Split Casings
- Bearing caps
- Bearing supports
Rotating Element Looseness
- Impellers
- Fans
- Bearings
- Couplings

## Slide 61: Characteristics of Looseness
Many Harmonics of running speed
Directional in nature; horizontal and vertical amplitudes may differ greatly
Occasional half-harmonics
Random, non-periodic time waveform
Broad based skirts on peaks in the Spectrum, possible elevated floor also

## Slide 62: Mechanical Looseness
Running speed harmonics
1X
2X
3X
4X
5X
6X
7X
8X
Multiple harmonics of running speed

## Slide 63: Mechanical Looseness
Looseness
Looseness shows up as
multiples of turning speed

## Slide 64: Rolling Element Bearing

## Slide 68: Why Does Bearing Fail?
1. Improper lubrication
2. Contaminated lubrication
3. Heavier loading from unbalance,
misalignment, bent shaft etc.
4. Improper handling or installation.
5. Old age (Surface fatigue) .

## Slide 69: Bearing Failure Stages
Earliest indications of bearing problems appear in the ultrasonic frequency ranging from 1,200k to 3,600 kCPM.
Spike Energy,PeakVue, HFD, and Shock Pulse evaluate these frequencies.
Stage - 1

## Slide 70: Stage - 2
Slight bearing defects begin to ring bearing component natural frequencies, which predominantly occur in 30k to 120K CPM range.
Sideband frequencies appear above and below nof stage 2.

## Slide 71: Stage - 3
Bearing defect frequencies and harmonics appear.
More defect frequencies appear and nos of sidebands grow, both around these and bearing natural frequencies.
When well-formed sidebands accompany bearing defect frequency harmonics
Bearing has to be replaced.

## Slide 72: Stage - 4
Towards the end-
Amplitude of 1X and other running speed harmonics will increase.
Discrete bearing defect and component natural frequencies actually begin to disappear and are replaced by random, broad band high frequency noise floor.
Amplitude of both high frequency noise floor and spike energy may decrease, but prior to failure, spike energy will usually grow to excessive amplitudes.

## Slide 73
Rolling element bearings
FTF = Fundamental Train Frequency
BSF = Ball Spin Frequency
BPFO = Ball Pass Frequency Outer race
BPFI = Ball Pass Frequency Inner race
FTF
.
.
1
2
1
.
d
D
cos
F
RPM
BSF
.
.
D
.
2
d
1
.
d
D
cos
F
2
RPM
BPFO
.
N
FTF
BPFI
.
N
(
RPM - FTF)
RPM = Shaft rotation
d = Rolling element diameter
D = Pitch diameter
N = No. of rolling elements
= Contact angle

## Slide 74
Rolling element bearings
What do the bearing frequencies mean?
If:
FTF = 0.381 * RPM
BSF = 1.981 * RPM
BPFO = 3.047 * RPM
BPFI = 4.952 * RPM
The cage rotates 0.381 revolutions
The ball spins 1.981 revolutions
4.952 balls pass an inner race defect
3.047 balls pass an outer race defect
During one shaft revolution:

## Slide 75: Anti-friction Bearing Faults
Ball Spin Frequency
(BSF)
Fundamental Train
Frequency
(FTF)
Ball Pass Frequency
Inner Race
(BPFI)
Ball Pass Frequency
Outer Race
(BPFO)
Four different bearing frequencies

## Slide 76: Envelope Detection
Repetitive bearing & gear mesh activity create vibration signals of much lower amplitude & higher frequencies than rotational and structural vibration signals
Enveloping – Filtering out the low frequency rotational vibration signals and to enhance the repetitive components of a bearing defect signals occurring in the bearing defect frequency range. Envelope detection is most common in rolling elements bearing and gear mesh analysis where a low amplitude repetitive vibration signal may be hidden by the machine’s rotational & structural vibration noise.
For e.g..
If a rolling element bearing has a defect on its outer race , each roller over-rolls the defect as it goes by and causes a small , repetitive vibration signal at the bearing defect frequency . However , this vibration signal is of such low energy that , with overall vibration monitoring , it is lost in the machine’s other rotational & structural vibration noise. Envelope detection filters out low rotational signals and enhances the bearing’s repetitive impact type signals to focus on repetitive events in the bearing defect frequency range( for eg repetitive bearing & gear tooth vibration signals)
In recent times this measurement method has proven to be a successful indicator of major class of machine problems . Faults in roller element bearings, defective teeth in gear boxes , paper mill felt discontinuities , and electric motor / stator problems are all applications for acceleration enveloping.

## Slide 77: Gear Box

## Slide 78
RPM1
RPM2
Z1
Z2
GMF (Gear Mesh Frequency)
Z1 .RPM1 = Z2 .RPM2
where Z = no. of teeth and RPM shaft speed
Gear box
Mating gears produce only one ‘Gear Mesh Frequency’

## Slide 79: Gear Box Defects
Tooth wear
Gear eccentricity & backlash
Gear misalignment
Cracked or broken tooth
Hunting tooth

## Slide 80
frequency
velocity
time
velocity
Spur gear produce vibration in radial direction and
helical gear produce in radial & axial directions.
Sideband spacing reveals the defective gear or pinion.
All analysis should be done at maximum load.
Z.Rps
Z.Rps+2 Rps
Z.Rps+Rps
Z.Rps-2 Rps
Z.Rps-Rps
1/Rps
Gear box

## Slide 81: Normal Spectrum
All peaks are of low amplitudes
No natural frequency of gear excited

## Slide 82: Tooth Wear
GMF may not change
High amplitudes of side bands
Presence of natural frequency of gear (fn)

## Slide 83: Gear Eccentricity & Backlash
Excites GMF, fn & their side bands
High amplitudes of side bands
Sideband spacing reveals the defective
gear or pinion.

## Slide 84: Gear Misalignment
Excites harmonics of GMF with side bands
Amplitudes 2GMF or 3GMF higher than 1GMF

## Slide 85: Cracked / Broken Tooth
High amplitudes of 1x RPM of gear or pinion
Excites gear natural frequency.
Time waveform indicates spikes at 1/RPM of broken or cracked tooth.
Amplitudes of impact spikes in time waveform will be higher than
that of 1xRPM in FFT.

## Slide 86: Hunting Tooth
1. Faults on both gear & pinion occured
during manufacturing.
2. Causes high vibration at low
frequencies (less than 600CPM)
3. Gear set emits growling sound.

## Slide 87
Hunting Tooth Frequency
It is the rate at which a tooth in one gear mates with a particular tooth in the other gear.
For well designed gearboxes HTF is low.
HTF = GMF . (lowest common prime factor) /(Z1.Z2)
Ex:
Z1 = 63, Z2 = 12
Z1 = 63 = 7.3.3
Z2 = 12 = 3.2.2
lowest common prime factor = 3
HTF = GMF. 3 / (63.12) = GMF / 252

## Slide 88
Belt Drive
BF (Belt Frequency) = Rps. .D / L
BF is the rotational frequency of the belt. Worn or mismatched belts will
produce radial vibration at BF and its harmonics. 2.BF is often dominant
with 2 sheaves in the system. BF is a subsyncronous vibration (below 1X).

## Slide 89
force
Eccentric sheaves will generate strong 1X radial components.
A common condition.
Looks like unbalance, but shows at both sheaves.
Belt Drive
Eccentric sheaves

## Slide 90
Belt Drive
Off-set
Angular
Axial vibrations at 1X and BF with harmonics.
Sheave misalignment

## Slide 91: Electrical Motors

## Slide 92
Asyncronous AC motors
Running speed:
where p = number of poles
f = line frequency
If no. of poles = 2.
The motor will have a sync. RPM of 3000
where fs = slip frequency
AC Motors
fs = RPMsync - RPM

## Slide 93
AC Motors
All electrical machines vibrates at 2 . line frequency.
The reasons are expanding and collapsing magnetic fields.
This vibration is normal (to a degree).
The amplitude is a measure of the quality of the construction.

## Slide 94
Coast Down Test
Vibration suddenly drops down after switching off the power
AC Motors

## Slide 95
AC Motors
Faults possible to detect with vibration analysis:
Rotor thermal bow
Air gap eccentricity
Loose rotor
Eccentric rotor
Loose windings
Necessary data:
No. of stator slots (SPF)
No. of rotor bars (RBPF)
Line frequency (LF)
Slip frequency (SF)

## Slide 96: ELECTRICAL PROBLEMS
Stator problems generate high amplitudes at 2FL (2X line frequency )
Stator eccentricity produces uneven stationary air gap, vibration is very directional
Soft foot can produce an eccentric stator
STATOR ECCENTRICITY
SHORTED LAMINATIONS
AND LOOSE IRON

## Slide 97: FREQUENCIES PRODUCED BY ELECTRICAL MOTORS.
Electrical line frequency.(FL) = 50Hz = 3000 cpm.
60HZ = 3600 cpm
No of poles. (P)
Rotor Bar Pass Frequency (Fb) = No of rotor bars x
Rotor rpm.
Synchronous speed (Ns) = 2xFL/P
Slip frequency ( FS )= Synchronous speed - Rotor rpm
Pole pass frequency (FP )= Slip Frequency x No of Poles.

## Slide 98: ELECTRICAL PROBLEMS
Loose stator coils in synchronous motors generate high amplitude at Coil Pass Frequency
The coil pass frequency will be surrounded by 1X RPM sidebands
SYNCHRONOUS MOTOR
(Loose Stator Coils)

## Slide 99: ELECTRICAL PROBLEMS
Phasing problems can cause excessive vibration at 2FL with 1/3 FL sidebands
Levels at 2FL can exceed 25 mm/sec if left uncorrected
Particular problem if the defective connector is only occasionally making contact
POWER SUPPLY
PHASE PROBLEMS
(Loose Connector)

## Slide 100: ELECTRICAL PROBLEMS
Eccentric rotors produce a rotating variable air gap, this induces pulsating vibration
Often requires zoom spectrum to separate 2FL and running speed harmonic
Common values of FP range from 20 - 120 CPM
ECCENTRIC ROTOR
(Variable Air Gap)

## Slide 101: ELECTRICAL PROBLEMS
DC motor problems can be detected by the higher than normal amplitudes at SCR firing rate
These problems include broken field windings
Fuse and control card problems can cause high amplitude peaks at frequencies of 1X to 5X Line Frequency
DC MOTOR PROBLEMS

## Slide 102: ELECTRICAL PROBLEMS
1X, 2X, 3X, RPM with pole pass frequency sidebands indicates rotor bar problems.
2X line frequency sidebands on rotor bar pass frequency (RBPF) indicates loose rotor bars.
Often high levels at 2X & 3X rotor bar pass frequency and only low level at 1X rotor bar pass frequency.
ROTOR PROBLEMS

## Slide 103
In order to find 2 X slip sidebands around FL, a analyzer
with high resolution, and preferably zoom around 50 Hz
is needed.
current clamp
Frequency analysis of input current
AC Motors

## Slide 104: Resonance

## Slide 105: RESONANCE
Resonance occurs when the Forcing Frequency coincides with a Natural Frequency
1800 phase change occurs when shaft speed passes through resonance
High amplitudes of vibration will be present when a system is in resonance

## Slide 107
IF YOUR ONLY TOOL IS A HAMMER, THEN EVERY OBJECT APPEARS TO BE A NAIL.